|  | Air core inductors Inductance in mH AWG d in mm D in mm h in mm DC resistance in m Weight in g 0,068 12 16 41 25 32 165 0,1 12 16 45 25 40 200 0,1 14 35,5 48 40 57 150 0,15 12 16 50 25 50 260 0,18 12 35,5 65 25 56 290 0,22 12 35,5 66 25 60 330 0,22 14 35,5 52 40 83 220 0,33 12 35,5 68 25 80 385 0,33 14 35,5 55 40 109 275 0,39 12 35,5 72 25 88 430 0,39 14 35,5 56 40 122 295 0,47 12 35,5 74 25 156 490 0,47 14 35,5 58 40 138 330 0,50 12 35,5 75 25 116 510 0,56 12 35,5 76 25 110 540 0,68 12 35,5 80 25 123 610 0,68 14 35,5 61 40 161 390 0,70 12 35,5 80 25 126 615 0,80 12 35,5 83 25 136 665 0,82 12 35,5 83 25 140 690 0,90 12 35,5 85 25 147 720 1,0 12 35,5 88 25 156 750 1,0 14 35,5 66 40 219 525 1,2 12 35,5 91 25 173 855 1,2 14 35,5 69 40 243 585 1,4 12 35,5 94 25 190 930 1,5 12 35,5 96 25 200 965 1,5 14 35,5 71 40 280 675 1,55 12 35,5 97 25 205 1015 1,6 12 35,5 98 25 220 1045 1,8 12 35,5 101 25 225 1070 1,8 14 35,5 74 40 306 740 1,9 12 35,5 103 25 232 1150 2,0 12 35,5 104 25 241 1175 2,1 12 35,5 105 25 245 1215 2,2 14 35,5 76 40 340 800 2,5 12 35,5 108 25 290 1355 2,7 12 35,5 113 25 297 1370 3,9 12 35,5 124 25 360 1800 4,0 12 35,5 125 25 370 1850 5,0 12 35,5 133 25 420 2100 5,0 14 35,5 93 40 560 1390 6,0 14 35,5 97 40 560 1540 7,0 14 35,5 101 40 680 1670 8,0 14 35,5 105 40 742 1840 15,0 14 35,5 122 40 1100 2620 |  |
| --- | --- | --- |

|  | Air core inductors Cutting edge inductor for the fastidious audiophile and serious high end loudspeaker system manufacturer. Paper and foil wound air core inductors for loudspeaker crossover networks. Unlike other brands, Jensen Capacitors foil wound inductors do not contain any polymers or plastics. They contain only natural materials providing a particular sonic benefit for the human ears. Carefully selected raw materials and a strictly controlled manufacturing process ensure uniform and high sonic quality. The high purity, oxygen-free copper foil and the dielectric consisting of very thin (20 µm) paper tissue made of special fine unbleached fibres, are wound onto a phenolic paper tube. To ensure high electrical and mechanical stability and long lifetime the windings are vacuum impregnated with mineral wax. The construction and the manufacturing process, during which the inductors are wound with a high and fully controlled winding tension, dried and impregnated under high vacuum ensure high and uniform sonic quality. Due to the large cross-sections (12 and 14 AWG) of the foil, the inductors have an extremely low AC/DC resistance resulting in reduced power loss, high current capability and extremely low stored charge. Negligible skin effect and flat inductance versus frequency curve from 20 Hz to 100 kHz are other important features. The leadouts are folded out of the copper foil in the winding itself, eliminating the need of welding or soldering, which are usually sources of undesired harmonic and phase distortions. As the impregnation wax has a melting point above 100°C, it is very consistent at room temperature, ensuring high mechanical and dimensional stability thus eliminating the FM distortion that may occur if the winding can flex or distort. Features: Conductor: High purity, oxygen free copper foil 0.15 x 20 mm. for AWG 12 and 0.06 x 35 mm for AWG 14. Dielectric: High density special paper, impregnated with mineral wax. Polypropylene, polyester (MYLAR), polycarbonate or polystyrene foil available only on request. Leadouts: Folded out of the conductor. Length depending on the dimension of the inductor but min. 50 mm. Inductance tolerance: ±5% ( for low inductance values ± 10%) |  |
| --- | --- | --- |