| Model | Adventure A 1-160 |
| --- | --- |
| Technical Data | Value | Unit |
| Cone material | Hexacone/Concave |
| Nominal impedance | 4 | Ohm |
| DC resistance | 3.4 | Ohm |
| Resonance freq. TS-para | 48 | Hz |
| Suspension compliance | 0.77 | mm/N |
| Mechanical Q | 2,75 |  |
| Electrical Q | 0.46 |  |
| Total Q | 0.4 |  |
| Total moving mass incl.air | 14.5 | g |
| Effective piston area | 137 | cm² |
| Voice coil diameter | 32 | mm |
| Voice coil former | Aluminium |  |
| Voice coil length | 11 | mm |
| Voice coil layers | 2 |  |
| Voice coil inductance | 0.36 | mH |
| Flux density | 1.15 | Tesla |
| Force factor | 5.7 | Tm |
| Height of the gap | 4 | mm |
| Diameter of magnet | 102 | mm |
| Height of magnet | 15 | mm |
| Sound press. level 1W1m | 88 | dB SPL |
| Nominal Power | 70 | W |
| VAS | 29 | dm³ |
| Frequency response | Fo-20000 | Hz |
| Crossover frequency | 1800 | Hz |
| Mounting depth | 50 | mm |
| Outer diameter | 165 | mm |
| Cut out diameter | 143 | mm |